Networking Lab #1

Goal:

Build a simple network utilizing a Linksys router and 2 computers.

Download and install both a web service and an ftp service. (Apache, Filezilla ). Verify connectivity between the computers and test the web server functionality.

Information:

Download and install both a web service and an ftp service. (Apache, Filezilla )

Build a simple network starting with both computers connected to the LAN and progressing to one computer on the LAN side and one computer on the WAN side. ( do not connect to the Sierra network at any time through the router).

Don’t forget to reset the router to factory defaults by pressing reset for 15 seconds, remove power while holding reset for 5 seconds, apply power and hold reset for an additional 15 seconds.

Router Settings:

Input a new password

Disable the wireless network

Enable the router to return a ping

Set up the WAN address

Setup the LAN address

Save the configuration to the router.

Disable the firewall on your machine.

Ping other machines and router ports within your network

Verify you can access the web server locally by going to 127.0.0.1 ( Loop Back address )

Enable IP Forwarding on your router for port 80 to your local machine

Verify you can access the other web server locally by going to your outside router address (178.168.X.X )

Test Filezilla and transfer files to the remote server to view in the web page.

Some problems you may encounter

Firewall on

No user permissions on the remote folder.

FTP is not pointed to the web folder.

No user account on the remote server.

Bring up the remote server web page and verify it displays your new web page.

Instructor sign off _________________