MH18
PC Identification

The ability to properly run software is a function of the type and configuration of a personal computer system.  Major determining factors include CPU type and speed, memory type(s) and size, BIOS features, chip set, adaptor cards, drive types and storage capabilities, as well as monitor, printer, and other peripheral device features.  In this lab you will identify the hardware complement of a generic PC.  

It is imperative that you employ proper ESD antistatic techniques while examining the PC.

1.  Connect the power cable from the PC.  Set the power switch OFF.
2.  Attach an anti-static band to your wrist and clip the connector to a non-painted exposed metal location on
     the chassis.
3.  Unlatch the case left side panel and remove it.  The PC may be turned on its side.  Be careful not to disturb
     any cables, connectors, or jumpers during the examination

4.  Locate and record the CPU type and manufacturer.
          a. How many processor cores does it have?
          b. What is its clock speed?
          c. What is the size of its L2 cache memory?
          d. How does it compare with more modern (more expensive) CPUs?
5.  Locate and record the DRAM memory type.
          a. What is the memory capacity of the each memory module (DIMM)?
          b. In what mode does it operate on the motherboard?
          c. What is the total amount of DRAM installed in the PC?
          d. What is the maximum installable amount of DRAM?
6.  Locate and identify the chip set.
7.  What type of battery backs up the real time clock (RTC)?
8.  Locate and record the storage Drive manufacturer and capacity for both internal and removable units.
          a. What type of interface does the internal SSD use (PCIe, SATA)?
          b. What type of interface is used for the removable HDD?
          c. How many drives are supported by its controller?
9.  Locate and record the removable media (optical) drive in the system.
           a. What media are compatible with this drive?
10. What form factor is the motherboard?  Who is the manufacturer?
           a. Record the type and number of expansion slots (PCI, PCIe).
11. Locate the back panel I/O ports.
          a. What types are supported?
          b. Are there other functions integrated on the motherboard?
12. Locate the Video ports.
          a. What type of video system is used?   Can it be upgraded?                                          
          b. What video ports are supported?
          d. Which port is connected to the monitor?  What is its maximum resolution?
13. How is the mouse attached to the system?  What is the mouse type?
14. How is the keyboard attached to the system?
15. Are there any other adaptor cards installed in the system?
16. What is the maximum wattage (power) rating of the power supply?  Is it UL listed?

17. Replace the case side panel.
18. Reconnect all the PC cables.
19. Boot the PC and verify that it is fully operational.
20. Instructor check point										________